Ciarán Johnson
(Non GenAI)
Main Memory

---
What is main memory?
Main memory is a piece of physical hardware within a personal computer which plays a vital part in the runnings of the computer

---
Main memory attributes
- Main memory of a personal computer has many attributes;
  - Each memory location has a unique address so that it can be directly accessed by the Central Processing Unit.
  - The number of unique addresses are determined by the size of the address bus so for 16bits there are 65,536 unique addresses and for 24bits there are 16.7 million unique addresses available

---
Main memory specifications
- The specifications of main memory are as follows;
  - For each unique memory address, the address can hold 8bits of one byte of information
  - A 16bit address bus requires 2bytes of data and each 16bit value is at a unique memory address

---
What main memory accomplishes
- Main memory holds the working data for both the applications and Operating system, some of this address space may be reserved and considered private for the Operating system, this is store secure data away from user accessible addresses.
- When you run out of main memory your operating system may use something called a pagefile where it offloads some of the data meant for the main memory into the Operating systems boot disk.

---
Architectural differences
- Main memory has two different types of architectures.
- Big endian,
  - Big endian consists of the most significant byte first followed by the least significant byte. e.g 0x65 0x78.
- Little endian,
  - Little endian consits of the least significant byte first followed by the most siginificant byte. e.g 0x78 0x65

---
Architectural compatibilites
Since main memory can be in two types, little endian and big endian, the architecural intercompatibility is required. This is achieved by the central processing unit which will convert the memory address to the type it supports and allows the personal computer to run correctly without any instability issues.

---
Conclussion
Main memory is a vital part of a computer and without it, we would not be able to have nice graphical applications or memory intensive application like Google Chrome or Firefox and we would be solely reliant on either a spinning platter or a Solid State Drive.